## Slide 1: R&S IM Spacing Sweep Development Plan
Nick Lalic
VNA Software Developer
Rohde & Schwarz North America

## Slide 2: Functionality
Measure intermodulation as a function of tone spacing (Initial, Final, Points)
Settings:
  Lower tone port
  Upper tone source (port, external generator)
  Receiving Port
  Source for Receiver Cal
  Center Frequency (Hz)
  Initial Tone Spacing (Hz)
  Final Tone Spacing (Hz)
  Points
  Power (dBm)
  IF BW (Hz)
  IF Selectivity (Normal | Medium | High)

## Slide 3: Functionality
Traces (output):
  <Type> <Side> <Order> <Location> Where
    Type: IM | IP | Tone
    Side: Upper | Lower | Major
    Order: 3 | 5 | 7 | 9
    Location: Input | Output
Traces displayed in VNA Firmware

## Slide 4: User Interface
Wizard
  Page 1 – Settings (ports, tone spacing, power, IF BW etc)
  Page 2 – Traces
  Pages 3-5 (Optional)
    Lower tone power cal
    Upper tone power cal
    Receiver power cal

## Slide 5: User Interface
Settings

## Slide 6: User Interface
Traces

## Slide 7: User Interface
Lower Tone Power Cal

## Slide 8: User Interface
Upper Tone Power Cal

## Slide 9: User Interface
Receiver Power Cal

## Slide 10: User Interface
Apply All

## Slide 11: Development Effort
Implement and Test ~10 SCPI commands in VNA driver:
  Set lower tone port
  Set upper tone source
  Set Receiver port
  Set tone spacing (iterative)
  Set IF BW Selectivity
  Set measured intermodulation products (order 3-7)
  Set trace type (IM, IP or Tone)
  Power cal lower tone
  Power cal upper tone
  Power cal receiver
Approximately 1 week

## Slide 12: Development Effort
Implement and Test data structures:
  Settings (lower port, upper source, receiver, …)
  Trace (name, type, order, side, location)
  Result, Results
Implement and Test classes:
  ConfigureIntermod(input: settings, traces, vna)
  SourcePowerCal(input: settings, vna)
  ReceiverPowerCal(input: settings, vna)
  MeasureOne(input: settings, current_spacing, vna) => Result
  Measure(input: settings, vna) => Results
  CreateTraces (input: traces, vna)
Implement and Test widgets (GUI):
  TracesModel
  TracesDelegate
Approximately 2 weeks

## Slide 13: Development Effort
Images (power cal)
Integration and Test
Installer
Real-world testing
Approximately 1 week
Total: Approximately 1 month development time to release
With other commitments: 1-2 months